## Slide 1: RF Network Analysis of the WEST ICRH Antenna with the Open-Source Python scikit-rf Package
RFPPC 2019
Julien Hillairet

## Slide 2: Summary
  Modern science is founded on reproducing experiments
  Closed-source codes lead to an obvious reproducibility problem. Research tools should ideally be open.
  Scikit-rf is an open-source Python package developed for RF/Microwave engineering
      Flexible and scalable library for network analysis and calibration
      Naturally compatible with the rich and modern scientific Python ecosystem, Jupyter notebooks and on-line virtualizations services
  Used to simulate the WEST ICRH antennas.
  Open-source and reproducible work-flow adds confidence in the fact that future staff could use and extend it

## Slide 3: WEST Antenna Matching Capacitors
  From full-wave model [1] of the capacitor at various positions
  Importing all .sNp files and plot Re[S21] for a subset of the frequency band:
import skrf as rf
capas_set = rf.NetworkSet.from_dir('S_Matrices/Antenna/Capacitor')
capas_set['20-80 MHz'].plot_s_re(m=1, n=0) # Indexing starts at 0 in Python
[1] data from W.Helou’s PhD, 2018

## Slide 4: Interpolating new networks
  Creating a new network interpolated from full-wave variations:
ntw = capas_set.interpolate_from_network(D_cylinders, new_value)
Repeating for other
new_value

## Slide 5: Creating equivalent lumped model
  Modelling the fact that capacitor is surrounded by outer conductor
def eq_capa(C, freq, z0, R, L, R1, C1, L1): # neglecting R_p
line = rf.media.DefinedGammaZ0(frequency=freq, z0=z0)
pre = line.resistor(R1) ** line.inductor(L1) ** line.shunt_capacitor(C1)
cap = line.resistor(R) ** line.inductor(L) ** line.capacitor(C)
post= line.shunt_capacitor(C1) ** line.resistor(R1) ** line.inductor(L1)
return pre ** cap ** post # ** is the connection operator in scikit-rf

## Slide 6: Model Parameter Extraction
  Assuming R1=R2, L1=L2, C1=C2
  Model Parameters are extracted using standard scipy.optimize package
Minimum bound (arbitrary) imposed for resistance values
  Parameters almost constant except Ls

## Slide 7: Benchmark models
  Equivalent lumped model fits well full-wave calculations
  Works even for low capacitance (in non-linear region)
  Error with full-wave reference < - 40 dB for all configurations

## Slide 8: Lumped Parameter Parameters
  Fixing the model parameters increases the error by ~10 dB on S11
      Especially for low capacitance values
      But still < -30dB
  S21 error still <-40dB
Specific Rs, Ls, R1, C1, L1
Unique Rs, Ls, R1, C1, L1

## Slide 9: WEST Capacitor Modeling with scikit-rf
Two possible numerical approaches for control
  Use equivalent lumped model (adjusted from full-wave)
      The control parameter is then the capacitance C of the assembly (which differs from the capacitance given by the manufacturer).
  Interpolate directly s-parameters from full-wave simulations:
      The control parameter is related to a geometrical distance between the capacitor electrodes

## Slide 10: Building Circuits: ½ WEST ICRH antenna example
  Scikit-rf allows building RF circuits from individual networks
connections = [
[(port1, 0), (window, 0)],
[(window, 1), (impedance_transformer, 0)],
[(impedance_transformer, 1), (bridge, 0)],
[(bridge, 1), (capa_upper, 0)],
[(bridge, 2), (capa_lower, 0)],
[(capa_upper, 1), (load_upper, 0)],
[(capa_lower, 1), (load_lower, 0)],
[(load_upper, 1), (ground_upper, 0)],
[(load_lower, 1), (ground_lower, 0)]
]
return rf.Circuit(connections)
  Resulting Network is calculated for all frequencies (vectorized)
  S-parameters are given for both Internal (at connections) and external (at ports)

## Slide 11: Building Circuits: ½ WEST ICRH antenna example
  Scikit-rf Circuit includes circuit’s graph visualization
  Previous Example leads to:
  Visualize each network port and char.imp.
  Convenient for checking mistakes

## Slide 12: Building Circuits: ½ WEST ICRH antenna example
  S-parameters accessible at connections  voltage and currents for a given excitation

## Slide 13: Building Circuits: ½ WEST ICRH antenna example
  Match Points Map for various loading cases: VSWR (Ctop, Cbot)
0.2+30j
0.5+30j
1.0+30j
1.5+30j

## Slide 14: Example: full WEST ICRH antenna
connections = [
# left conjugate T
[(left_port, 0), (left_window, 0)],
[(left_window, 1), (left_impedance_transformer, 0)],
[(left_impedance_transformer, 1), (left_bridge, 0)],
[(left_bridge, 1), (capa_left_upper, 0)],
[(left_bridge, 2), (capa_left_lower, 0)],
# right conjugate T
[(right_port, 0), (right_window, 0)],
[(right_window, 1), (right_impedance_transformer, 0)],
[(right_impedance_transformer, 1), (right_bridge, 0)],
[(right_bridge, 1), (capa_right_upper, 0)],
[(right_bridge, 2), (capa_right_lower, 0)],
# front face
[(capa_left_upper, 1), (front_face, 0)],
[(capa_left_lower, 1), (front_face, 2)],
[(capa_right_upper, 1), (front_face, 1)],
[(capa_right_lower, 1), (front_face, 3)],
]
circuit = rf.Circuit(connections)

## Slide 15: WEST ICRH Matching
  Using the scipy optimization framework, the 4 capacitances can be deduced to match the antenna for a given loading

## Slide 16: Scikit-rf functionalities
ntw1
Stiching Networks
  Combines two networks that cover different frequency into a single network
Arithmetic Operations
  Element-wise operations on s-parameters
      Ex: Phase difference
  Comparison operators (==)
Interpolation, resampling
ntw = stich(ntw1, ntw2)
ntw = ntw1 + ntw2
Scikit-rf documentation
f
ntw2
ntw
ntw = ntw1 – ntw2
ntw = ntw1 * ntw2
ntw = ntw1 / ntw2

## Slide 17: Scikit-rf functionalities
Cascading Networks
  Effect of mismatched port impedances taken into account
Deembedding Networks
ntw2
ntw1
ntw = ntw1 ** ntw2
ntw
ntw2
ntw1
ntw
ntw1 = ntw ** ntw2.inv
Scikit-rf documentation